## Slide 1: Ulaştırma ve Altyapı Bakanlığı DHMİ Genel Müdürlüğü
Havalimanları Slot Koordinasyon Merkezi (HSKM) Başmüdürlüğü

## Slide 2: GCR (GENERAL AVIATION SLOT CLEARANCE REQUEST)

## Slide 3
*the slot clearance process for General Aviation (GA) & Business Aviation (BA) operations
Information in this Guide is extracted from Appendix K of the IATA SSIM (Standard Schedules Information Manual) IATA General (Aviation) Clearance Request (GCR) format.

## Slide 4: GCR Message Principles
• only uses ICAO codes for aircraft and airports.
• reference ----REG or FLT
• For GCR communication using E-mail the GCR message should be in plain text placed directly in the E-mail body. No attachments or special characters should be used.
• in UTC
• in single day format only
• does not contain a frequency rate (day of week) indicator.

## Slide 5
Following flights are exempted from slot coordination procedure:
 Government flights (service type E)
 Ambulance flights (service type I)
 State flights (service type I)
 Military flights (service type W)
 Search and Rescue flights
 Flights for Humanitarian reasons
The following Service Types will be used for requests concerning General/Business aviation.
 Private/General Aviation (D)
 Business/Corporate Aviation / Air Taxi (N)
 Positioning /ferry (P)
 Technical stop (X)

## Slide 6: Requesting a GA/BA slot
The GCR message must be composed of 3 parts:
1. HEADER
2. DATA LINE(S)
3. FOOTER

## Slide 7: 1. HEADER

## Slide 8: 2. DATA LINE(S) NVHLEE 31JUL 018CRJ2 YPDN1920 D
3. FOOTER
Any non-standard format text must be put in the footer preceded by a “SI” or “GI”.
SI - stands for special information at end of message.
GI - stands for general information at end of message.

## Slide 9
The GCR message uses the following action codes:
Operator
C - Schedule to be changed
D - Delete schedule
N - New schedule
R - Revised schedule
Coordinator
H – Holding
K – Confirmation
U - Refusal
W - Unable to reconcile flight information
X - Cancellation
Note: Unlike SCR, there is no action code “O” (Offer) in GCR. The nearest available slot will be confirmed by coordinator using the action code “K”.

## Slide 10
GIR
(General Aviation Information Request/Reply) Message
The GIR request for a time period is limited to one day only, a range of dates is not permitted.
GIRs include only the GA/BA flights held with aircraft registration (REG) and are shown with a generic two letter code GN.

## Slide 11
GIR
/FLT
LPPT
QGN1215 GN1215 07MAY
SI
GIR
/FLT
LPPT
HGN1215 GN1215 07MAY 012CL60 GLRB0130 0230EGGW DD/ RE.GLWDC/
************************************************************************
GIR
/REG
LPPT
QGLWDC 07MAY
SI
GIR
/FLT
LPPT
HGLWDC 07MAY 012CL60 GLRB0130 0230EGGW DD

## Slide 12
Note:
The Generic Code for carrier code is- GN
The Generic Code for General aviation aircraft is- GAA
The Generic Code for Airports is- XUD

## Slide 13
Message type for operation under registration and domestic flight to two level 3 airports;
GCR
/REG
EDDF
N HBIEV 08JUN 010G159 0900EDDM D
EDDM
NHBIEV 08JUN 010G159 EDDF 1000 D
SI
GCR
/FLT
EDDF
N ABC123 08JUN 010G159 0900EDDM D
EDDM
NABC 08JUN 010G159 EDDF1000 D
SI

## Slide 14
Message Use/ Flows
GCR /REG LTAI NXYZAT 02MAY 018GLF5 OOMS1110 1145LIMG NN SI GI
GCR /REG LTAI KXYZAT 02MAY 018GLF5 OOMS1110 1145LIMG NN / IDA.LTAIAGN0015000 IDD.LTAIDGN0016000 TA.T2 TD.T2/ SI GI

## Slide 15
GCR /REG LTAI NTCABC 25APR 014GRJ LMML1400 D / RE.XYZTC / SI Line number: 4 A new and different aircraft registration defined via tags GI BRGDS
GCR /FLT LTBJ KXYZ005 XYZ005 26APR 022A20N LTFE0900 1000LTFE DD / IDA.LTBJAXYZ000500 IDD.LTBJDXYZ000500 RE.SDFGH TA.D TD.D/ SI
SI UCAK TIPININ ICAO KODU SSIM DA BELIRTILMEDIGINDEN EN YAKIN SI UCAK TIPI SECILMISTIR. UCAK TIPI HAWKER C90 DIR.

## Slide 16
GCR /REG LTBJ N TCABC-1 07MAY 009CL35 1200LTBA N NTCABC-1 07MAY 009CL35 LTBA1355 P GI
GCR /REG LTBA CXYZTM 15MAY 010CL30 LIPZ1325 15002LKPR DD RPLM001 PLM002 15MAY 010CL30 LIPX1320 10301LTFM NN SI GI
** could not be handled
GIR /FLT LTBJ QABC005 ABC005 28APR10MAY 0000507 *GIR requests are limited one day only

## Slide 17
Note: Changes of registration in the same GCR message will not be accepted.
When a change of aircraft registration is required for a GA/BA flight with already confirmed slots, even when all other SSIM line data remain the same, the aircraft operator and/or handler should DELETE the already confirmed slots in one GCR and a new GCR request for NEW slots should follow with the new a/c registration

## Slide 18
Teşekkür Ederim

## Slide 19
DHMİ GENEL MÜDÜRLÜĞÜ HAVALİMANLARI SLOT KOORDİNASYON MERKEZİ (HSKM) BAŞMÜDÜRLÜĞÜ
ADRES: İstanbul Havalimanı İmrahor Mah.
Vecihi Hurkus Cad. No: 6 Kat:2 (VIP Yanı) 34275
Arnavutköy-ISTANBUL
TEL: 0 212 891 74 00
FAX: 0 212 891 7404
SMA-SCR mesajları için : tr.slot@dhmi.gov.tr
E-MAIL: dhmi.slot@dhmi.gov.tr

## Slide 20
SLOT KOORDİNASYON ŞUBE MÜDÜRLÜĞÜ
TEL:
SKM Dönemsel Planlama: 0 212 891 74 55
SKM Monitoring Ünitesi: 0 212 891 74 75
SKM Operasyon: 0 212 891 74 85
E-MAIL:
SKM Dönemsel Planlama: dhmi.sccplanning@dhmi.gov.tr
SKM Monitoring Ünitesi: dhmi.sccmonitoring@dhmi.gov.tr
SKM Operasyon: dhmi.sccoperation@dhmi.gov.tr
FAX: 0 212 891 74 74
SMA-SCR mesajları için : tr.slot@dhmi.gov.tr